## Slide 1: FT900 Alexa Demo
For PanL Smart Home

## Slide 2
ft900
microphone
speaker
alexa sdk
ft900 alexa demo
for PanL Smart Home
ETHERNET
WIFI
RS485
rpi 3b+

## Slide 3
1
2
3
4
5
6
7
8
Multiple FT900 clients connected to different Alexa instances/accounts
Alexa Virtualization

## Slide 4
User Presses FT900 Button
User Talks to Alexa on FT900 Microphone
FT900 Sends Alexa Request to RPI
RPI Relays Alexa Request to the Cloud
RPI Relays Alexa Response to FT900
FT900 Receives Alexa Response from RPI
FT900 Plays Alexa Response on Speaker
User presses down a button on FT900 to start voice
recording and releases it to stop recording.
User commands Alexa to turn on a smart home device
and FT900 saves the voice recording on SD card.
FT900 sends the compressed voice recording to RPI
and RPI receives the voice recording and decompresses it.
RPI sends the Alexa request to the cloud
and receives the AI-generated Alexa response.
RPI decodes Alexa response from MP3 format to raw
PCM format, compresses it and sends it to FT900.
FT900 receives compressed audio from RPI,
decompresses it and saves it to SD card.
FT900 reads audio from SD card
and plays it on the connected speaker.
1
2
3
4
5
6
7

## Slide 5
Ask information, control devices
Set alarms, timers
Play music, audio book, live news
DIALOG
ALERTS
CONTENT

## Slide 6: FT900 Alexa Demo
Demonstrates FT900 as an Amazon Echo Dot
  Just like Amazon Echo, users can issue voice commands to Alexa and hear Alexa’s voice responses generated by Alexa’s speech recognition and natural language processing in the cloud.
Uses RPI as Alexa gateway
  FT900 (Alexa client) communicates with a Raspberry PI 3B+ (Alexa gateway), which relays voice requests and voice responses to and from the Alexa cloud.
  RPI runs a customized version of Amazon’s official Alexa Voice Service (AVS) SDK, written in C++.
Added Alexa Virtualization feature
  RPI supports Alexa Virtualization feature enabling multiple MCU clients to simultaneously access Alexa using multiple Alexa instances and different Amazon accounts.

## Slide 7: PanL Smart Home with built-in Alexa
Targets FTDI/Bridgetek’s PanL Smart Home products
  PanL Hub and PanL Display.
  PanL Hub, which runs on RPI, will act as the Alexa gateway while the PanL Display, which runs on FT900, will act as the Alexa client.
Having Alexa built-in to PanL products
  Allow customers to talk directly to Alexa via PanL
  No need for Amazon Echo devices
  Make PanL more marketable

## Slide 8: FT900 Alexa Client
FT900 Alexa Demo Application
BUTTON
GPIO
Alexa AVS library
MEMORY WRAPPER
AUDIO
Speaker, Microphone, Compression
SDHost
I2S
fatfs
Ethernet
lwip
Free RTOS
COMMUNICATION WRAPPER
UART
I2C
SPI
at
ESP32
RS485
sdcard
flash
rs485
ethernet
wifi

## Slide 9: RPI Alexa Gateway
AVS SDK SampleApp
Connection Handler
AVS SDK library
Audio
Compression
Request Handler
Response
Handler
Audio
Decoding
Response Hook
Request
Hook
Audio Rate
Conversion
Client Handler
Request Manager
Response Manager
Port Audio
Microphone

## Slide 10: RPI Alexa Gateway
AVS SDK SampleApp
AVS SDK library
GStreamer Media Player
Media
Player
Capability Agents
Speech Synthesizer
Alerts
Audio
Player
Attachment ReaderSource
IStream
Source
BaseStreamSource

## Slide 11: Gstreamer Audio Pipeline Hooking
appsrc
decoder
decoded
Queue
converter
volume
resample
caps
equalizer
audio sink
tee
audio queue
app queue
app sink
fake sink
Added a tee branch to output to both appsink and audiosink
Replaced audiosink with fakesink to disable audio playback

## Slide 12: Different Alexa instances & Amazon accounts
app
app
app
Alexa Manager
Script
automated configuration & execution
AlexaClientSDKConfig.json
db
PORT_BASE
AlexaClientSDKConfig2.json
db2
PORT_BASE + 1
AlexaClientSDKConfig3.json
db3
PORT_BASE + 2